## Slide 1
Memory Hierarchy
Lecture 7
February 4, 2013
Mohammad Hammoud
CS15-346 Perspectives in Computer Architecture

## Slide 2: Objectives
Discussion on Memory Hierarchy
Motivation
Cache Management Policies: Placement, Location, Replacement & Write Policies
Cache Miss Types
Memory-Level Parallelism and Prefetching

## Slide 3: Objectives
Discussion on Memory Hierarchy
Motivation
Cache Management Policies: Placement, Location, Replacement & Write Policies
Cache Miss Types
Memory-Level Parallelism and Prefetching

## Slide 4: Why Memory Hierarchy?
CPU versus memory speeds
  CPU speed grew at the rate of 55% annually
  Memory speed grew at the rate of only 7% annually
This created a CPU-Memory gap with some implications
  In the past, a load instruction could get the required datum from memory in 1 cycle
  In recent systems, this might take 100s of cycles
The CPU can stall for much of the time, especially if it runs out of independent instructions
Hence, it is critical for performance that most data are supplied to the CPU with low latencies
The memory hierarchy provides such a support!

## Slide 5: What is Memory Hierarchy?
The memory hierarchy consists of relatively small and volatile storages referred to as caches
The concept of a cache is universal
  Caches as software constructs
  Caches as hardware components
In embedded systems, the memory hierarchy often consists of software-managed storage referred to as scratchpad memory
Our focus is on hardware caches that exist between CPU and the main memory
P
L1-I
L1-D
P
L1-I
L1-D
L2 Cache
L3 Cache
Main Memory
Chip Boundary
2-3 GHZ
16KB-64KB
2-4 Cycles
512KB-8MB
6-15 Cycles
4MB-32MB
30-50 Cycles
1GB-4GB
300+ Cycles

## Slide 6: Why Caches are Effective?
Computer programs exhibit properties
One of the most important properties that we regularly observe is the principle of locality
  Programs tend to reuse data and instructions they have used recently
Two different types of locality have been observed
  Temporal locality: recently accessed items are likely to be accessed in the near future
  Spatial locality: items that are near one another are likely to be accessed one after the other
Due to the principle of locality, caches are an effective structure to keep code and data closer to CPU
70-95% cache hit rates are not uncommon today!
Notes: A widely held rule of thumb is that a program spends 90% of its execution time in only 10% of the code

## Slide 7: Objectives
Discussion on Memory Hierarchy
Motivation
Cache Management Policies: Placement, Location, Replacement & Write Policies
Cache Miss Types
Memory-Level Parallelism and Prefetching

## Slide 8: Basic Cache Architecture
A cache structure can be thought of as a table
A Table
Number of columns
Number of rows
Cell Size
A Cache
Associativity (number of ways)
Number of sets
Cache Block Size

## Slide 9: How to Manage a Cache?
To manage a cache, four main policies should be implemented
  This policy decides where a block can be placed in the cache
Placement Policy
  This policy decides which block needs to be evicted to make room for a new block
Replacement Policy
  This policy decides when a modified block should be propagated to the lower level component in the hierarchy
Write Policy
1
3
4
  This policy decides where and how to locate a block after being placed in the cache
Location Policy
2

## Slide 10: Cache Management
Cache Management Policies
Placement Policy
Location Policy
Replacement Policy
Write Policy

## Slide 11: Placement Policy and Cache Organizations
The organization of the cache determines the placement of a block
Caches can be organized in three ways:
A block can be placed at
only 1 way, but at any set
A Direct-Mapped Cache
A block can be placed at only 1 set, but at any way
A Fully-Associative Cache
A Set-Associative Cache
A block can be placed at multiple ways, at any set
Notes: Set Index = Block address % number of sets

## Slide 12: Direct Mapped vs. Fully Associative vs. Set-Associative
Direct-Mapped Cache:
  Suffers from conflicts
  Search complexity = O(1)
  Easy to implement
Fully-Associative Cache:
  Does not suffer from conflicts
  Search complexity = O(Cache Size/Block Size)
  Expensive to implement
Set-Associative Cache:
  More resistant to conflicts than a direct-mapped cache
  Search complexity = O(Cache Size/(Block Size * # of Sets)
  Much cheaper to implement than a fully-associative cache

## Slide 13: Cache Management
Cache Management Policies
Placement Policy
Location Policy
Replacement Policy
Write Policy

## Slide 14: Location Policy
As the rationale behind caching is to keep data for future accesses, blocks must be locatable
A cache employs three steps to locate a block:
  Determine the set to which the block has been placed
  Access the set to determine if any of the blocks in the set matches the one being requested
  If the requested block is found, locate the desired word, and return it to CPU
Tag
Address:

## Slide 15: Locating a Block in a Cache
Decoder
Tag | Index | offset
Match
Match
OR
Hit/Miss
Sense Amps
Select a Block
Select byte/word
Requested Byte/Word
Tag Array
Data Array
Address

## Slide 16: Physical versus Virtual Addresses
The addresses of the physical memory hierarchy are physical addresses
P
L1-I
L1-D
P
L1-I
L1-D
L2 Cache
L3 Cache
Main Memory
Chip Boundary
The addresses that programs generate are virtual addresses
A major issue that has to do with locating cache blocks is virtual memory

## Slide 17: Virtual Memory
Virtual memory (vM) is a well-known technique supported in most general-purpose OSs
  IBM introduced vM into its mainframe OS (i.e., OS/370) in 1972
  vM was introduced into Unix as part of 3BSD Unix in 1979
  Microsoft included vM into Windows as part of Windows NT3.1 in 1993
  vM was included into MacOS as part of release X in 2000
vM allows a process to run even if it does not fit within the available physical memory
The basic idea of virtual memory is that each process is provided with its own virtual address space
Notes: In the earliest days, either a process fits a memory or it couldn’t be run.

## Slide 18: Translating Virtual Addresses to Physical Addresses
The virtual address space of each process is translated to the physical address space that the physical memory uses
The translation of virtual page addresses to physical addresses is maintained in a software data structure called the page table
---
---
---
---
---
0K-8k
8K-16k
16K-24k
32K-40k
44K-52k
52K-60k
60K-68k
68K-76k
0K-8k
8K-16k
16K-24k
Physical Address Space
Page #
Offset
Virtual Pages
Virtual Address
Physical Pages
Virtual Address Space
Notes: - A page is a contiguous range of addresses

## Slide 19: Page Tables
Each process has its own page table
  Each process has its own view of the virtual address space
1000
2000
Virtual Memory of Program 1 on Machine M
1500
3000
5000
Physical Memory of Machine M
1000
4000
Virtual Memory of Program 2 on Machine M
Not Mapped
Virtual Page | Physical Page
--- | ---
1000 | 5000
--- | ---
2000 | 1500
--- | ---
Virtual Page | Physical Page
--- | ---
1000 | Not Mapped
--- | ---
4000 | 3000
--- | ---

## Slide 20: A Problem with Page Table
The virtual-to-physical translation must be done on every memory reference
All modern computers use virtual addresses of at least 32 bits, with 64 bits becoming increasingly common
With, say, a 4-KB page size
  A 32-bit address space will have 1 million pages
  A 64-bit address space will have more than you want to contemplate!
This will significantly slow down page translation and degrade performance
However, most programs tend to make a large number of references to a small number of pages
What about keeping the small fraction of the page table entries in a small cache?

## Slide 21: Translation Lookaside Buffer
To speed up paging, computers are equipped with a small hardware device for caching virtual-to-physical translations so as to bypass page tables
Such a device is referred to as Translation Lookaside Buffer (TLB)
Typical TLBs:
  Size: 12 - 4,096 entries
  Hit time: 0.5 - 1 clock cycle
  Miss penalty: 10 - 100 clock cycles
  Miss rate: 0.01 - 1%
Valid | Virtual Page | Modified | Protection | Page Frame
1 | 140 | 1 | RW | 31
1 | 20 | 0 | R | 38
1 | 130 | 1 | RW | 14

## Slide 22: TLBs and Cache Addressing
Cache addressing can be carried out using 1 of 3 options:
  Cache is indexed using the index bits of the physical address
  Tag bits of the physical address are stored in the cache’s tag array
Physical Addressing
  Cache is indexed using the index bits of the virtual address
  Tag bits of the virtual address are stored in the cache’s tag array
Virtual Addressing
  Cache is indexed using the index bits of the virtual address
  Tag bits of the physical address are stored in the cache’s tag array
Mixed Addressing
1
2
3

## Slide 23: TLBs and Cache Addressing
TLB
L1 Cache
VA
PA
Physical Addressing:
Physically Indexed + Physically Tagged
The TLB access time is directly added to the cache access time
Adding a few cycles to each L1 cache access can significantly degrade performance
TLB
L1 Cache
VA
PA
Virtual Addressing:
Virtually Indexed + Virtually Tagged
The TLB and the L1 cache can be accessed in parallel
The cache cannot be shared since each process has its own virtual view
Mixed Addressing:
Virtually Indexed + Physically Tagged
Observation: Page offset bits are the same in virtual and physical addresses  Ensure that the cache index bits are a subset of these bits
The cache can be accessed immediately and in parallel with TLB
L1 cache size is limited
TLB
L1 Cache
VA
PA
Tag Match?
PT

## Slide 24: Mixed Addressing: A Working Example
Assume a 4KB page
  We need as the page offset
Assume a 32-byte cache block size
  We use the lowest as the block offset
Therefore, we can use up to 12 – 5 = 7 bits for cache indexing
  We can have 27 = 128 sets
For a direct-mapped cache, we can support an L1 cache size of
For a 4-way associative cache, we can support an L1 cache size of
More generally, the maximum cache size can be computed as follows:

## Slide 25: Cache Management
Cache Management Policies
Placement Policy
Location Policy
Replacement Policy
Write Policy

## Slide 26: Replacement Policy
When a new block is to be placed in the cache, a resident block of the cache needs to be evicted first
Criterion for an optimum replacement [Belady, 1966]:
  The block that will be accessed the farthest in the future should be the one that is evicted
Optimum replacement is not implementable
Hence, most caches implement a different criterion:
  The block that was accessed the farthest back in the past is the one that is evicted
  This is commonly known as the Least Recently Used (LRU) policy

## Slide 27: LRU
LRU exploits temporal locality as recently accessed data tend to be accessed again in the future
In practice LRU performs very well, although it trails the performance of optimum replacement
There is a case in which LRU performance is pathological:
  When a program accesses more blocks in a circular pattern than what the cache can hold
  Assume a program accesses blocks A, B, C, A, B, C, A, and so on, all mapping to a single cache set on a cache that has a 2-way associativity
A | 
B | A
C | B
A | C
B | A
C | B
A | C
Access A
Access B
Access C
Access A
Access B
Access C
Access A
. . .
. . .
Miss
Miss
Miss
Miss
Miss
Miss
Miss

## Slide 28: Pseudo-LRU Replacement
LRU is expensive to implement for highly-associative caches
An approximation to LRU is to keep track of only a few Most Recently Used (MRU) blocks, and evict a block from not-MRU set, either randomly or based on a certain algorithm
Tree-based pseudo-LRU adopts such a strategy [Al-Zoubi et al. 2004]
1
0
A
B
0
C
D
Access: 0 = Left and 1 = Right. Replacement: 0 = Right and 1 = Left
Initially
1
0
A
B
0
C
D
Access Block B
0
1
A
B
0
C
D
Replacement
0
1
Evict!

## Slide 29: Cache Management
Cache Management Policies
Placement Policy
Location Policy
Replacement Policy
Write Policy

## Slide 30: Write Policy
A main question in cache design is:
  When should a change to a cache block be propagated to the lower level component in the hierarchy?
The strategy that addresses this question is what is known as the write policy
There are two choices to employ a write policy
  Write-through
  Write-back
In a write-through policy, any change to a block is immediately propagated to the lower level component in the hierarchy
In a write-back policy, only when an altered block is evicted, change is propagated to the lower level component in the hierarchy

## Slide 31: Write-Through vs. Write-Back
Which write policy to choose and at which memory hierarchy component?
Pros and Cons:
  Off-chip bandwidth is a limited resource, while on-chip bandwidth tends to be much higher
  Error Correcting Code (ECC), which enables error correction, is more expensive than parity bits, which can detect but not correct errors
Typical choice:
  L1 cache uses a write-through policy so as to use simpler parity bits
  L2 cache uses a write-back policy so as to conserve off-chip bandwidth, but needs to be protected with ECC
Write-Through | Write-Back
Highly consumes bandwidth usage | Conserve bandwidth usage
Write-Through | Write-Back
Highly consumes bandwidth usage | Conserve bandwidth usage
More resistant to soft errors | Less resistant to soft errors
Notes: L1 latency is very critical to system performance

## Slide 32: Objectives
Discussion on Memory Hierarchy
Motivation
Cache Management Policies: Placement, Location, Replacement & Write Policies
Cache Miss Types
Memory-Level Parallelism and Prefetching

## Slide 33: Basic Types of Cache Misses
The performance of a CPU is impacted by the number of cache hits versus the number of cache misses
There are various basic types of cache misses, known as the 3 Cs:
How to distinguish between 3 Cs?
  The first miss to a memory block is a compulsory miss, subsequent misses are not
  Conflict misses = # of misses of an n-way associative cache # of misses of fully-associative cache (not always true!)
  The remaining misses are the capacity misses
Compulsory Misses | Conflict Misses | Capacity Misses
Misses that are required to bring blocks into the cache for the first time | Misses that occur due to limited cache associativity | Misses that occur due to limited cache size

## Slide 34: Impact of Cache Parameters on Cache Misses
Parameter | Compulsory Misses | Conflict Misses | Capacity Misses
Larger Cache Size | Unchanged | Unchanged | Decreased
Cache parameters affect the different types of misses as follows:
Parameter | Compulsory Misses | Conflict Misses | Capacity Misses
Larger Cache Size | Unchanged | Unchanged | Decreased
Larger Block Size | Decreased | Decreased/Increased | Decreased/Increased
Parameter | Compulsory Misses | Conflict Misses | Capacity Misses
Larger Cache Size | Unchanged | Unchanged | Decreased
Larger Block Size | Decreased | Decreased/Increased | Decreased/Increased
Larger Associativity | Unchanged | Decreased | Unchanged

## Slide 35: Other Types of Cache Misses
There are other types of misses that are mentioned less frequently in literature
Coherence misses matter a lot in multiprocessor systems (e.g., CMPs) and are one of the sources of bottlenecks in scalability of parallel programs
System-related misses also matter overall
  When a process is suspended due to a context switch, its cache state is perturbed by an interfering entity (another thread/process or the OS)
  When the process resumes, it will suffer from new cache misses to restore cache state that has been perturbed
Coherence Misses | System-Related Misses
Misses that occur due to the need to keep the cache coherent in shared memory multiprocessor systems | Misses that occur due to system activities such as system calls, interrupts, and context switches

## Slide 36: Context Switch Misses [Liu et al. 2008]
Natural misses (or basic misses) are reduced with larger cache size
Context switch misses (Replaced + Reordered) increase with larger cache size (until total working sets fit)

## Slide 37: Objectives
Discussion on Memory Hierarchy
Motivation: Why Memory Hierarchy and Why Caches are Effective
Cache Management Policies: Placement, Location, Replacement & Write Policies
Cache Performance: Cache Miss Types
Memory-Level Parallelism and Prefetching

## Slide 38: Memory Level Parallelism
In early caches, memory accesses will stall until an access that misses in the cache is satisfied
  This might tremendously hurt performance
To overcome this problem, modern cache architectures use a structure referred to as Miss Status Handling Registers (MSHR)
When a cache access misses, an MSHR entry is allocated to keep track of the status of the miss
  This frees up the cache to service new accesses
A cache that uses MSHR is called a non-blocking or lockup-free cache and what is offered by such a cache is denoted as memory-level parallelism
Memory-level parallelism is required to implement certain architecture features (e.g., prefetching)

## Slide 39: Prefetching
A technique which attempts to bring data into the cache before the program accesses them
Prefetching comes at the expense of extra bandwidth usage
  Some blocks that are prefetched may never be used by the processor
Many CPUs provide a special instruction for specifying an address to prefetch
There are two types of prefetching:
  Software prefetching: CPU’s special prefetching instruction is inserted by the compiler into the code
  Hardware prefetching: A hardware engine is used to detect access patterns and prefetch data
Basic techniques:
  Sequential Prefetching: detects and prefetches accesses to contiguous locations
  Stride Prefetching: detects and prefetches accesses that are s-cache block apart between consecutive accesses

## Slide 40
Thank You!
Next Class:
Chip Multicores, Challenges and Opportunities