## Slide 1: Distributed Systems CS 15-440
Networking- Part II
Lecture 3, August 28, 2017
Mohammad Hammoud

## Slide 2: Today…
Last Session:
  Networking- Part I
    Network Types
    Networking Principles: Layering
Today’s Session:
  Networking- Part II
    Networking Principles: Encapsulation, Routing, and Congestion Control
Announcements:
  PS1 is out; it is due on September 11th
  Eid Al Adha break is from August 31st to September 7th
    No recitation on August 31st

## Slide 3: Packet Encapsulation
Encapsulation is a technique to pack and unpack data packets in a layered architecture

## Slide 4: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 5: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 6: Physical Layer
Physical layer protocols transmit a sequence of bits over a transmission medium
  Modulate the bits into signals that can be transmitted over the medium
Transmission Medium | Type of signal transmitted
Twisted-pair (Ethernet cable) | Electrical signal
Fiber Optic Circuits | Light signal
Wireless channel | Electro-magnetic signal
A physical layer protocol
Data-link layer protocol
Transmission Medium
Bits
Signal

## Slide 7: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 8: Data-link Layer
Protocols in data-link layer ensure that packets are delivered from one host to another within a local network
Data-link layer protocols provide two main functionalities:
  How to coordinate between the transmitters such that packets are successfully received?
    Coordination
  How to identify another host on the local network?
    Addressing over local networks

## Slide 9: Coordination at Data-link Layer
A packet is not received successfully at the receiver if a sender transmits the data when another sender’s transmission is active
  The packet is said to have experienced collision if it is not successfully received at the receiver
Collision is avoided by sensing the medium before transmission

## Slide 10: Addressing over Local Networks
Each device that is connected to a network has a unique address called Medium Access Control (MAC) address
  MAC addresses are six bytes long
    e.g., 2A:D4:AB:FD:EF:8D
Approach:
  Data-link layer broadcasts the packet over the medium
  Receiver reads the packet header and checks if the packet is addressed to it
x
x

## Slide 11: Layers that We Will Study Today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 12: Network Layer
Network layer protocols perform the role of routing
  They ensure that a packet is routed from the source machine to the destination machine
  Packets may traverse different LANs to reach the destination
Internet Protocol (IP) is a widely-used network layer protocol
  IP addresses are typically used to identify machines
Destination
Source
Router

## Slide 13: Router
A router is a device that forwards the packets between multiple networks
Routers are connected to two or more networks
  Each network interface is connected to a LAN or a host
Packet travels up until the network layer on the router
LAN-3
Int-3
Int-2
A Router
LAN-2
LAN-1
Physical
Data-link
Network
Transport
Application
Source machine
Physical
Data-link
Network
Transport
Application
Dest machine
Physical
Data-link
Network
Router
Int-1

## Slide 14: Routing Algorithm
Packets have to be transmitted in a series of hops through the routers
  The series of hops that a packet takes is known as a route
Routing algorithm is responsible for determining the routes for the transmission of packets
Challenges for designing routing algorithms in the Internet:
  Performance: The traffic across different networks vary
  Router failures: Routers in the Internet may fail
S
D
R1
R2
R4
R4

## Slide 15: Routing Algorithm (Cont’d)
Routing algorithms have two activities
  Determine the next-hop taken by each packet
    The algorithm should be fast and efficient
  Dynamically update connectivity information
    Maintain the knowledge of the network by monitoring routers and traffic
The above activities are distributed throughout the network
  Routing decisions are made on an hop-by-hop basis
  Information about possible next-hop routers is stored locally
  Information is updated periodically
We will study a simple routing algorithm called “Distance Vector Algorithm”

## Slide 16: Distance Vector Algorithm
Distance Vector (DV) uses graph theoretical algorithms to find the best route in the network
  It uses a well-known shortest path algorithm called Bellman-Ford algorithm
Two activities for the DV routing algorithm:
  Determining the best next-hop at each router
  Dynamically update connectivity information at all the routers

## Slide 17: Distance Vector Algorithm – Next-hop Determination
Each router maintains a routing table that consists of:
  Destination: The destination IP of the packet
  Link: The outgoing link on which the packet should be forwarded
  Cost: The distance between the router and the destination
    E.g., Cost can be estimated as the delay for the packet to reach the destination
Router looks up the table to determine the best next-hop
Routing table at a router A
To
Link
Cost
A
B
C
D
E
local
1
1
3
1
0
1
2
1
2
A
B
D
1
3
Links
Routers
Hosts or local networks
C
2
E
4

## Slide 18: Routing Tables for an Example Scenario
A
B
E
D
C
1
2
3
4
6
5
Routers
Hosts or local networks
Links
Routings from A
Routings from B
Routings from C
To
Link
Cost
To
Link
Cost
To
Link
Cost
A
B
C
D
E
local
1
1
3
1
0
1
2
1
2
A
B
C
D
E
1
local
2
1
4
1
0
1
2
1
A
B
C
D
E
2
2
local
5
5
2
1
0
2
1
Routings from D
Routings from E
To
Link
Cost
To
Link
Cost
A
B
C
D
E
3
3
6
local
6
1
2
2
0
1
A
B
C
D
E
4
4
5
6
local
2
1
1
1
0

## Slide 19: Distance Vector Algorithm – Updating the Connectivity Information
Connectivity is updated by exchanging routing table
Router Information Protocol (RIP) is used for sending update messages
  Send routing table to neighboring routers
    Periodically, or when local table changes
  When a neighbor’s routing table is received:
Case | If the received routing table … | Updates to the local routing table
1 | Has a new destination that is not in the local routing table | Update the Cost and Link
2 | Has a better-cost route to a destination in the local routing table | Update the Cost
3 | Has a more recent information | Update the Cost and Link

## Slide 20
Pseudocode for RIP
Send: Each t seconds or when Tl changes, send Tl on each non-faulty outgoing link
Receive: Whenever a routing table Tr is received on link n:
for all rows Rr in Tr {
if (Rr.link != n) {
Rr.cost = Rr.cost + 1; // Update cost
Rr.link = n; // Update next-hop
if (Rr.destination is not in Tl) {
add Rr to Tl; // add new destination to Tl
}
else for all rows Rl in Tl {
if (Rr.destination = Rl.destination) {
// Rr.cost < Rl.cost : remote node has better route
// Rl.link = n : information is more recent
if (Rr.cost < Rl.cost OR Rl.link = n) {
Rl = Rr;
}
}
}
}
}
A
B
E
D
C
1
2
3
4
6
5
Routing table at router A
To
Link
Cost
A
D
local
3
0
1
Tl at A
C
3
3
Routing table of router B
To
Link
Cost
A
B
local
1
1
0
C
2
1
Tr recvd @ A from B on link n=1
Case 1
Case 2
Case 3
Notes: 20
Ask:
What happens when a link is broken?
Will this surely converge even if link breaks?
How can you take care of link-quality? Say link A-B is 10Gbps Ethernet link and link A-C is 2Mbps wireless link.

## Slide 21: Summary: Routing over Internet
Each machine over the Internet is identified by an IP Address
Source machine transmits the packet over its local network
Intermediate routers examine the packet, and forward it to the best next-hop router
If the destination is directly attached to the local network of a router, the router forwards the packet over the respective local network
Routers exchange information to keep an up-to-date information about the network

## Slide 22: Layers that we will study today
Physical layer
Data-link layer
Network layer
Transport layer

## Slide 23: Transport Layer
Transport layer protocols provide end-to-end communication for applications
This is the lowest layer where messages (rather than packets) are handled
Messages are addressed to communication ports attached to the processes
  Transport layer multiplexes each
  packet received to its respective port
P1
P3
P2
Transport layer protocol
Destination machine
Network layer protocol

## Slide 24: Simple Transport Layer Protocols
Simple transport protocols provide the following services:
  Multiplexing Service
  Connection-less Communication: The sender and receiver processes do not initiate a connection before sending the message
    Each message is encapsulated in a packet (also called as datagram)
    Messages at the receiver can be in different order than the one sent by the sender
    E.g., User Datagram Protocol (UDP)

## Slide 25: Advanced Transport Layer Protocols
Advanced transport layer protocols typically provide more services than simple multiplexing
Transmission Control Protocol (TCP) is a widely-used protocol that provides three additional services:
  Connection-oriented Communication
  Reliability
  Congestion Control

## Slide 26: 1. Connection-Oriented Communication
Sender and receiver will handshake before sending the messages
  Handshake helps to set-up connection parameters, and to allocate resources at destination to receive packets
Destination provides in-order delivery of messages to the intended process
  Destination will buffer the packets until previous packets are received
  It will then deliver packets to the process in the order that the sender had used
P1
P3
P2
TCP protocol
Destination machine
P1
P3
P1
TCP protocol
Source machine
Shall I send?
OK. Start sending

## Slide 27: 2. Reliability
Packets may be lost in the network due to buffer overflows at the router or transmission error(s)
In TCP, destination sends an ACK to the sender
  If ACK is not received at the sender, the sender will infer a packet error, and retransmit the packet

## Slide 28: 3. Congestion Control
The capacity of a network is limited by the individual communication links and routers
  Limited buffer space and link-bandwidth
What happens if a source transmits packets at a rate that is greater than the capacity of the network?
  Packets drop at intermediate routers
  Corresponding ACKs will NOT be received at the source
  The source retransmits
  More packets build-up on the router queue
  The network collapses

## Slide 29: 3. Congestion Control (Cont’d)
To avoid congestion, two functionalities can be adopted
  Detect congestion at routers
    If a router expects a buffer overflow, it typically follows one of two strategies:
      It drops packets and lets sources regulate upon observing packet losses
      It sends an “Explicit Congestion Notification (ECN)” packet to sources
  Regulate input at sources
    If the TCP-sender concludes congestion (e.g., it receives an ECN packet), then it reduces its sending rate
Notes: What is the best layer for congestion control?
Do you know any other protocol similar to TCP that is widely used?
When/where is congestion control important, where is it not?

## Slide 30: Recap: Introduction to Networking – Learning Objectives
You will identify how computers over the Internet communicate
Specifically, after the two lectures in networking you will be able to:
  Identify different types of networks
  Describe networking principles such as layering, encapsulation, and packet-switching
  Examine how packets are routed and how congestion is controlled
  Analyze scalability, reliability, and fault-tolerance over the Internet

## Slide 31: Next class
Remote Procedure Calls- Part I